## Slide 1: CS162 Operating Systems and Systems Programming Lecture 17 Performance Storage Devices, Queueing Theory
October 24, 2018
Prof. Ion Stoica
http://cs162.eecs.Berkeley.edu

## Slide 2: Review: Basic Performance Concepts
Response Time or Latency: Time to perform an operation
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: NB/s, Networks: Mb/s, Arithmetic: GFLOP/s
Start up or “Overhead”: time to initiate an operation
Most I/O operations are roughly linear in n bytes
  Latency(n) = Overhead + n/Bandwidth

## Slide 3: Example (Fast Network)
Consider a 1 Gb/s link (B = 125 MB/s)
  With a startup cost S = 1 ms
  Latency(n) = S + n/B
  Bandwidth = n/(S + n/B) = B*n/(B*S + n) = B/(B*S/n + 1)

## Slide 4: Example (Fast Network)
Consider a 1 Gb/s link (B = 125 MB/s)
  With a startup cost S = 1 ms
  Bandwidth = B/(B*S/n + 1)
  half-power point occurs at n=S*B  Bandwidth = B/2

## Slide 5: Example: at 10 ms startup (like Disk)
  n = 1,250,000 bytes!

## Slide 6: What Determines Peak BW for I/O ?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire): 1.6 Gb/s full duplex (200 MB/s)
  USB 3.0 – 5 Gb/s
  Thunderbolt 3 – 40 Gb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path…

## Slide 7: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for sequential access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (5-20x disk)
  Block level random access
  Good performance for reads; worse for random writes
  Erasure requirement in large blocks
  Wear patterns issue

## Slide 8: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)

## Slide 9: Review: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surface
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Seek time = 4-8ms
One rotation = 1-2ms (3600-7200 RPM)

## Slide 10: Review: Magnetic Disks
Cylinders: all the tracks under the head at a given point on all surface
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Disk Latency = Queueing Time + Controller time +
Seek Time + Rotation Time + Xfer Time

## Slide 11: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000 (ms/minute) / 7200(rev/min) ~= 8ms
  Transfer rate of 4MByte/s, sector size of 1 Kbyte  1024 bytes/4×106 (bytes/s) = 256 × 10-6 sec  .26 ms
Read sector from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 10ms to fetch/put data: 100 KByte/sec
Read sector from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 5ms to fetch/put data: 200 KByte/sec
Read next sector on same track:
  Transfer (0.26ms): 4 MByte/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 12: (Lots of) Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
…

## Slide 13: Solid State Disks (SSDs)
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advances in capacity and cost ever since!

## Slide 14: SSD Architecture – Reads
  Read 4 KB Page: ~25 usec
  No seek or rotational latency
  Transfer time: transfer a 4KB page
    SATA: 300-600MB/s => ~4 x103 b / 400 x 106 bps => 10 us
  Latency = Queuing Time + Controller time + Xfer Time
  Highest Bandwidth: Sequential OR Random reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
DRAM
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
SATA

## Slide 15: SSD Architecture – Writes
  Writing data is complex! (~200μs – 1.7ms )
  Can only write empty pages in a block
  Erasing a block takes ~1.5ms
  Controller maintains pool of empty blocks by coalescing used pages (read, erase, write), also reserves some % of capacity
Rule of thumb: writes 10x reads, erasure 10x writes
https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 16: Amusing calculation: is a full Kindle heavier than an empty one?
Actually, “Yes”, but not by much
Flash works by trapping electrons:
  So, erased state lower energy than written state
Assuming that:
  Kindle has 4GB flash
  ½ of all bits in full Kindle are in high-energy state
  High-energy state about 10-15 joules higher
  Then: Full Kindle is 1 attogram (10-18gram) heavier (Using E = mc2)
Of course, this is less than most sensitive scale can measure (it can measure 10-9 grams)
Of course, this weight difference overwhelmed by battery discharge, weight from getting warm, ….
According to John Kubiatowicz (New York Times, Oct 24, 2011)

## Slide 17: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD

## Slide 18: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD
  Asymmetric block write performance: read pg/erase/write pg
    Controller garbage collection (GC) algorithms have major effect on performance
  Limited drive lifetime
    1-10K writes/page for MLC NAND
    Avg failure rate is 6 years, life expectancy is 9–11 years
These are changing rapidly!
No longer true!

## Slide 19: Seagate Enterprise
10 TB (2016)
7 platters, 14 heads
7200 RPMs
6 Gbps SATA /12Gbps SAS interface
220MB/s transfer rate, cache size: 256MB
Helium filled: reduce friction and power usage
Price: $500 ($0.05/GB)
IBM Personal Computer/AT (1986)
30 MB hard disk
30-40ms seek time
0.7-1 MB/s (est.)
Price: $500 ($17K/GB, 340,000x more expensive !!)

## Slide 20: Largest SSDs
60TB (2016)
Dual port: 16Gbs
Seq reads: 1.5GB/s
Seq writes: 1GB/s
Random Read Ops (IOPS): 150K
Price: ~ $20K ($0.33/GB)

## Slide 21: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%
# of ops
Fixed overhead
time per op

## Slide 22: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 23: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/TS) - operations per sec
Arrival rate: (λ = 1/TA) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA
TS
Tq

## Slide 24: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TS/TA)
Delivered Throughput
0
1
1
time
Queue delay
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TS/TA)
Empty Queue
Saturation
Unbounded

## Slide 25: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
TQ
TS
Q depth
Server
Arrivals

## Slide 26: So how do we model the burstiness of arrival?
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Chart: 
| 0.001 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 10.0
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Likelihood of an event occurring is independent of how long we’ve been waiting
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)

## Slide 27: Background: General Use of Random Distributions
Server spends variable time (T) with customers
  Mean (Average) m = p(T)T
  Variance (stddev2) 2 = p(T)(T-m)2 = p(T)T2-m2
  Squared coefficient of variance: C = 2/m2 Aggregate description of the distribution
Important values of C:
  No variance or deterministic  C=0
  “Memoryless” or exponential  C=1
    Past tells nothing about future
    Poisson process – purely or completely random process
    Many complex systems (or aggregates) are well described as memoryless
  Disk response times C  1.5 (majority seeks < average)
Mean
(m)
mean
Memoryless
Distribution
of service times


## Slide 28: Administrivia
Midterm 2 coming up on Mon 10/29 5:00-6:30PM
  All topics up to and including Lecture 17
    Focus will be on Lectures 11 – 17 and associated readings
    Projects 1 and 2
    Homework 0 – 2
  Closed book
  2 pages hand-written notes both sides

## Slide 29: break

## Slide 30: Introduction to Queuing Theory
Departures
Arrivals
Queuing System
What about queuing time??
  Let’s apply some queuing theory
  Queuing Theory applies to long term, steady state behavior  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Queue
Controller
Disk
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 31: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
The average number of jobs/tasks in the system (N) is equal to arrival time / throughput (λ) times the response time (L)
  N (jobs) = λ (jobs/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  Instantaneous variations, but it washes out in the average
  Overall, requests match departures
arrivals
departures
N
λ
L

## Slide 32: Example
λ = 1
L = 5
0
1
2
3
4
5
6
7
8
16
9
10
11
12
13
14
15
time
Jobs
L = 5
N = 5 jobs
A: N = λ x L
E.g., N = λ x L = 5

## Slide 33: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
Job i
L(1)

## Slide 34: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
What is the system occupancy, i.e., average
number of jobs in the system?
Job i

## Slide 35: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
S = S(1) + S(2) + … + S(k) = L(1) + L(2) + … + L(k)
S(k)

## Slide 36: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Average occupancy (Navg) = S/T
Job i
S= area

## Slide 37: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = S/T = (L(1) + … + L(k))/T
S(k)

## Slide 38: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (L(1) + … + L(k))/T = (Ntotal/T)*(L(1) + … + L(k))/Ntotal
S(k)

## Slide 39: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = (Ntotal/T)*(L(1) + … + L(k))/Ntotal = λavg × Lavg
S(k)

## Slide 40: Little’s Theorem: Proof Sketch
time
T
arrivals
departures
N
λ
L
N(t)
L(i) = response time of job i
N(t) = number of jobs in system
at time t
S(i) = L(i) * 1 = L(i)
Job i
S(1)
S(2)
Navg = λavg × Lavg
S(k)

## Slide 41: A Little Queuing Theory: Some Results (1/2)
Assumptions:
  System in equilibrium; No limit to the queue
  Time between successive arrivals is random and memoryless
Parameters that describe our system:
  : mean number of arriving customers/second
  Tser: mean time to service a customer (“m”)
  C: squared coefficient of variance = 2/m2
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Parameters we wish to compute:
  Tq: Time spent in queue
  Lq: Length of queue =   Tq (by Little’s law)
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser

## Slide 42: A Little Queuing Theory: Some Results (2/2)
Parameters that describe our system:
  : mean number of arriving customers/second = 1/TA
  Tser: mean time to service a customer (“m”)
  C: squared coefficient of variance = 2/m2
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Parameters we wish to compute:
  Tq: Time spent in queue
  Lq: Length of queue =   Tq (by Little’s law)
Results (M: Poisson arrival process, 1 server):
  Memoryless service time distribution (C = 1): Called an M/M/1 queue
    Tq = Tser x u/(1 – u)
  General service time distribution (no restrictions): Called an M/G/1 queue
    Tq = Tser x ½(1+C) x u/(1 – u))
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser

## Slide 43: A Little Queuing Theory: An Example (1/2)
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller + seek + rotation + transfer)
Questions:
  How utilized is the disk (server utilization)? Ans:, u = Tser
  What is the average time spent in the queue? Ans: Tq
  What is the number of requests in the queue? Ans: Lq
  What is the avg response time for disk request? Ans: Tsys = Tq + Tser

## Slide 44: A Little Queuing Theory: An Example (2/2)
Questions:
  How utilized is the disk (server utilization)? Ans:, u = Tser
  What is the average time spent in the queue? Ans: Tq
  What is the number of requests in the queue? Ans: Lq
  What is the avg response time for disk request? Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
u (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05s
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 45: Queuing Theory Resources
Resources page contains Queueing Theory Resources (under Readings):
  Scanned pages from Patterson and Hennessy book that gives further discussion and simple proof for general equation: https://cs162.eecs.berkeley.edu/static/readings/patterson_queue.pdf
  A complete website full of resources: http://web2.uwindsor.ca/math/hlynka/qonline.html
Some previous midterms with queueing theory questions
Assume that Queueing Theory is fair game for Midterm III

## Slide 46: Summary
Disk Performance:
  Queuing time + Controller + Seek + Rotational + Transfer
  Rotational latency: on average ½ rotation
  Transfer time: spec of disk depends on rotation speed and bit storage density
Devices have complex interaction and performance characteristics
  Response time (Latency) = Queue + Overhead + Transfer
    Effective BW = BW * T/(S+T)
  HDD: Queuing time + controller + seek + rotation + transfer
  SDD: Queuing time + controller + transfer (erasure & wear)
Systems (e.g., file system) designed to optimize performance and reliability
  Relative to performance characteristics of underlying device
Bursts & High Utilization introduce queuing delays
Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x u/(1 – u))

## Slide 47: Optimize I/O Performance
How to improve performance?
  Make everything faster 
  More decoupled (Parallelism) systems
  Do other useful work while waiting
    Multiple independent buses or controllers
  Optimize the bottleneck to increase service rate
    Use the queue to optimize the service
Queues absorb bursts and smooth the flow
Add admission control (finite queues)
  Limits delays, but may introduce unfairness and livelock
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 48: When is Disk Performance Highest?
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (reordering queues—one moment)
OK to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?
Other techniques:
  Reduce overhead through user level drivers
  Reduce the impact of I/O delays by doing other useful work in the meantime