## Slide 1: Exception
Yubin Xia
IPADS, SJTU
ACKs: Some slides are adapted from the textbook's original slides and Frans's OS course notes

## Slide 2: Review: IPC
Cooperating processes need inter-process communication (IPC)
Two models of IPC
  Shared memory
  Message passing
In POSIX
  Pipe, message passing, signal, shared memory, semaphore, etc.
LRPC: Lightweight RPC

## Slide 3: Concepts
Exception
  refers to an illegal program action
Interrupt
  refers to a signal generated by a hardware device
System call
  a user program can ask for an operating system service

## Slide 4: Exception

## Slide 5: CPU's 'fetch-execute' cycle
Fetch instruction at IP
Advance IP to next instruction
Decode the fetched instruction
Execute the decoded instruction
Interrupt?
no
Save context
Get INTR ID
Lookup ISR
Execute ISR
yes
IRET
User
Program
IP
ld
add
st
mul
ld
sub
bne
add
jmp
…

## Slide 6: Exception Table
1. Each type of event has a unique exception number k
2. Exception table entry k points to a function (exception handler).
3. Handler k is called each time exception k occurs.
Exception
table
0
1
2
...
n-1
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers

## Slide 7: Exception Table

## Slide 8: Some Exception on Intel CPU
Notes: Questions:
What is the difference between an exception and an interrupt caused by hardware?
Can system call be implemented by using int 0x81 or 0x82?

## Slide 9: IDT (or Trap Vector in xv6)
IDT: interrupt descriptor table
  Another name of exception table
  Has 256 entries
  Each giving the %cs and %eip to be used when handling the corresponding interrupt
System call
  A program invokes int n
    int is for interrupt (not integer)
    n specifies the index into the IDT

## Slide 10: Exception Handler
The processor pushes a return address on the stack, the return address is:
  either the current instruction (e.g., page fault)
  or the next instruction (e.g., hardware interrupt)
The processor also pushes some additional processor state onto the stack
  Will be necessary to restart the interrupted program when the handler returns
    e.g. the current condition codes

## Slide 11: Exception Handler
All items are pushed onto the kernel stack
  Rather than onto the user's stack
    If control is being transferred from a user program to the kernel
Exception handlers run in kernel mode
  Means they have complete access to all system resources

## Slide 12: Kernel Stack

## Slide 13: Stack Change
Question: why not use user's stack?

## Slide 14: Sources of Events cause User->Kernel
Device interrupt: external
  Nonmaskable interrupt (NMI) input pin
  Interrupt (INTR) input pin
Software interrupt: execution of the Interrupt instruction
  E.g., INT
Program faults: If some error condition occur by the execution of an instruction.
  E.g.,divide-by-zero interrupt

## Slide 15: What Has to Happen?
Must save the processor's registers for future transparent resume
Must be set up for execution in the kernel
Must chose a place for the kernel to start executing
Must be able to retrieve information about the event, e.g., system call arguments
Must all be done securely
Must maintain isolation of user processes and the kernel

## Slide 16: Return From Interrupt Handler in Kernel
The 'iret' instruction
  Restore the process's context
  Switch from kernel mode to user mode
  Continue the execution of user's process

## Slide 17: Simplified: Call OS Services from Apps and Devices
Exception
Table
Application (CPU)
OS
I/O Device
Services
Exception
Interrupt
Notes: Question: what if

## Slide 18: xv6: Initialize the Exception Table

## Slide 19: xv6: Trap

## Slide 20: Three Crucial Data-structures
The Global Descriptor Table (GDT)
    defines the system's memory-segments and their access-privileges, which the CPU has the duty to enforce
The Interrupt Descriptor Table (IDT)
    defines entry-points for the various code-routines that will handle all 'interrupts' and 'exceptions‘
The Task-State Segment (TSS)
    holds the values for registers SS and ESP that will get loaded by the CPU upon entering kernel-mode

## Slide 21: How does CPU find GDT/IDT?
Two dedicated registers: GDTR and IDTR
Both have identical 48-bit formats:
Segment Base Address
Segment Limit
0
15
16
47
Privileged instructions: LGDT and LIDT used to set these register-values
Unprivileged instructions: SGDT and SIDT used for reading register-values
Kernel must setup these registers during system startup (set-and-forget)

## Slide 22: How does CPU find the TSS?
Dedicated system segment-register TR holds a descriptor's offset into the GDT
TR
GDTR
GDT
TSS
The CPU knows the layout
of fields in the Task-State
Segment
The kernel must set up the
GDT and TSS structures
and must load the GDTR
and the TR registers

## Slide 23: Interrupt

## Slide 24: Varying Terminology for Intel
Interrupts (asynchronous, device generated)
  Maskable: device-generated, associated with IRQs (interrupt request lines); may be temporarily disabled (still pending)
  Nonmaskable: some critical hardware failures
Exceptions (synchronous, from software)
  Processor-detected
    Faults – correctable (restartable); e.g. page fault
    Traps – no reexecution needed; e.g. breakpoint
    Aborts – severe error; process usually terminated (by signal)
  Programmed exceptions (software interrupts)
    int (system call), int3 (breakpoint)
    into (overflow), bounds (address check)

## Slide 25: Terms
Vector, Interrupt vector, Trap number
IRQ: Interrupt Request
  Note: Soft IRQ is a mechanism to implement bottom half, it has nothing to do with IRQ!
Interrupt, trap, fault, exception
Software interrupt / system call
IDT: Interrupt Descriptor Table
ISP: Interrupt Service Procedure

## Slide 26: Intel-Reserved ID-Numbers
Of the 256 possible interrupt ID numbers, Intel reserves the first 32 for 'exceptions'
OS's such as Linux are free to use the remaining 224 available interrupt ID numbers for their own purposes (e.g., for service-requests from external devices, or for other purposes such as system-calls)
Examples:
  0: divide-overflow fault
  6: Undefined Opcode
  7: Coprocessor Not Available
  11: Segment-Not-Present fault
  12: Stack fault
  13: General Protection Exception
  14: Page-Fault Exception

## Slide 27: Interrupts
Interrupts are similar to system calls, except devices generate them at any time
There is hardware on the motherboard to signal the CPU when a device needs attention (e.g., the user has typed a character on the keyboard)
We must program the device to generate an interrupt, and arrange that a CPU receives the interrupt

## Slide 28: Interrupt Response Sequence

## Slide 29: Early Boards
PIC (Programmable Interrupt Controller)
  picirq.c
  8259A chip
  Each PIC handles 8 interrupts, and multiplex them on the interrupt pin of the processor
  PIC can be cascaded
    Master: 0 to 7
    Slave: 8 to 15
  Read timer.c for timer init

## Slide 30: 8259A Programmable Interrupt Controller (PIC)
8259A is a 28-pin integrated circuit which was designed specifically for the 8088/8086 microprocessors
Notes: ❚ The 28 pins of the 8259A include:
1. Data pins D0-D7 - connected to the data bus to allow programming
2. IR0-IR7 - 8 interrupt inputs
3. CAS0-CAS2 - cascade lines (used in multiple 8259A systems)
4. SP/EN - functions as data buffer enable output (when buffered mode)
or as an input to program the 8259A as a master or slave
5. A0 - input which selects different command words in the 8259A
❚ Usually IR0 has the highest priority and IR7 the least priority.
❚ Fully nested interrupts are supported (higher priority interrupts may
interrupt the interrupt service routine of a lower priority interrupt) if bit 4 of
ICW is set. (Refer to data sheets for further details.)

## Slide 31
Interrupt Hardware
x86
CPU
Master
PIC
(8259)
Slave
PIC
(8259)
INTR
Programmable Interval-Timer
Keyboard Controller
Real-Time Clock
Legacy PC Design
(for single-proc
systems)
SCSI Disk
Ethernet
I/O devices have (unique or shared) Interrupt Request Lines (IRQs)
IRQs are mapped by special hardware to interrupt vectors, and passed to the CPU
This hardware is called a Programmable Interrupt Controller (PIC)
IRQs

## Slide 32: APIC, IO-APIC, LAPIC
Advanced PIC (APIC) for SMP systems
  Used in all modern systems
  Interrupts “routed” to CPU over system bus
  IPI: inter-processor interrupt
Local APIC (LAPIC) versus “frontend” IO-APIC
  Devices connect to front-end IO-APIC
  IO-APIC communicates (over bus) with Local APIC
Interrupt routing (like on a network)
  Allows broadcast or selective routing of interrupts
  Ability to distribute interrupt handling load
  Routes to lowest priority process
    Special register: Task Priority Register (TPR), i.e., locking
  Arbitrates (round-robin) if equal priority

## Slide 33: Multiple Processors
Multi-CORE CPU
CPU
0
CPU
1
I/O
APIC
LOCAL
APIC
LOCAL
APIC
Advanced Programmable Interrupt Controller is needed to
perform 'routing' of I/O requests from peripherals to CPUs
(The legacy PICs are masked when the APICs are enabled)
Notes: External hardware INTerrupt sources are routed to pins of the IO APIC. These include motherboard sources such as the 8254 timer, as well asISA/PCI card slots. INTerrupts are "collected" by this part, and forwarded via the APIC bus to one or more CPUs when they occur.

## Slide 34: Multi-processor PC Boards
Two parts in XV6
  IO APIC, for the I/O system
    ioapic.c
  Local APIC, for each processor
    lapic.c
XV6 is designed for multi-processor
  Each processor must be programmed to receive interrupts

## Slide 35: Assigning IRQs to Devices
IRQ assignment is hardware-dependent
  Sometimes it's hardwired, sometimes it's set physically, sometimes it's programmable
  PCI bus usually assigns IRQs at boot
Some IRQs are fixed by the architecture
  IRQ0: Interval timer
  IRQ2: Cascade pin for 8259A
Linux device drivers request IRQs when the device is opened
  Note: especially useful for dynamically-loaded drivers, such as for USB or PCMCIA devices
  Two devices that aren't used at the same time can share an IRQ, even if the hardware doesn't support simultaneous sharing

## Slide 36: Some Details on IRQ
Some hardware IRQs are pre-determined
  E.g., the system timer (IRQ0), Keyboard controller (IRQ1), floppy controller (IRQ6), real-time clock (IRQ8) and Math Co-processor (IRQ13)
Most others are 'user' determined
  via hardware (with jumpers)
  via software (such as installable drivers) with firmware (PNP)
IRQs that are usually available for add-on devices:
  Modem (IRQ5), printer (IRQ7), Sound Card (IRQ9/IRQ10)
  Video Card (IRQ11) and PS/2 mouse (IRQ12)
  IRQ3 and IRQ4 are usually reserved for serial ports
  IRQ14 and IRQ15 are used for the IDE (primary and secondary)

## Slide 37: Assigning Vectors to IRQs
Vector: index (0-255) into interrupt descriptor table
Vectors are usually IRQ# + 32
  Below 32 reserved for non-maskable intr & exceptions
  Maskable interrupts can be assigned as needed
  Vector 128 used for syscall
  Vectors 251-255 used for IPI