## Slide 1: CS162 Operating Systems and Systems Programming Lecture 21 Layering, E2E Argument
November 14th, 2018
Prof. Ion Stoica
http://cs162.eecs.Berkeley.edu

## Slide 2: Example: What’s in a Search Query?
Complex interaction of multiple components in multiple administrative domains
Datacenter
Load
balancer
Ad Server
DNS
Servers
Search
Index
DNS
request
create
result
page

## Slide 3: Goals for Today
Layering
End-to-end arguments
Some slides generated from Vern Paxson and Scott Shenker lecture notes

## Slide 4: Why is Networking Important?
Virtually all apps you use communicate over network
  Many times main functionality is implemented remotely (e.g., Google services, Amazon, Facebook, Twitter, …)
Thus, connectivity is key service provided by an OS
  Many times, connectivity issues  among top complaints

## Slide 5: Why is Networking Important?
Virtually all apps you use communicate over network
  Many times main functionality is implemented remotely (e.g., Google services, Amazon, Facebook, Twitter, …)
Thus, connectivity is key service provided by an OS
  Many times, connectivity issues  among top complaints
Some of the hottest opportunities in the OS space:
  Optimize OS for network elements (e.g., intrusion detection, firewalls)
  OSes for Software Defined Networks (SDNs)

## Slide 6: Network Concepts
Network (interface) card/controller: hardware that physically connects a computer to the network
A computer can have more than one networking cards
  E.g., one card for wired network, and one for wireless network
Process
A
OS
Process
B
OS
Network cards

## Slide 7: Network Concepts (cont’d)
Typically, each network card is associated two addresses:
  Media Access Control (MAC), or physical, address
  IP, or network, address (can be shared by network cards on same host)
Process
A
OS
Process
B
OS
Network cards
IP Addr1
MAC Addr1
IP Addr2
MAC Addr2
IP Addr3
MAC Addr3

## Slide 8: Network Concepts (cont’d)
MAC address: 48-bit unique identifier assigned by card vendor
IP Address: 32-bit (or 128-bit for IPv6) address assigned by network administrator or dynamically when computer connects to network
Process
A
OS
Process
B
OS
Network cards
IP Addr1
MAC Addr1
IP Addr2
MAC Addr2
IP Addr3
MAC Addr3

## Slide 9: Network Concepts (cont’d)
Connection: communication channel between two processes
Each endpoint is identified by a port number
  Port number: 16-bit identifier assigned by app or OS
  Globally, an endpoint is identified by (IP address, port number)
Process
A
OS
Process
B
OS
Network cards
IP Addr1
MAC Addr1
IP Addr2
MAC Addr2
IP Addr3
MAC Addr3
Connection
PortA
PortB

## Slide 10: Main Network Functionalities
Delivery: deliver packets between any two hosts in the Internet
  E.g., how do you deliver a packet from a host in Berkeley to a host in Tokyo?
Reliability: tolerate packet losses
  E.g., how do you ensure all bits of a file are delivered in the presence of packet loses?
Flow control: avoid overflowing the receiver buffer
  Recall our bounded buffer example: stop sender from overflowing receiver’s buffer
    E.g., how do you ensure that a sever that can send at 10Gbps doesn’t overwhelm a mobile phone?
Congestion control: avoid overflowing the buffer of a router along the path
  What happens if this happens?

## Slide 11: Protocol Standardization
Ensure communicating hosts speak the same protocol
  Standardization to enable multiple implementations
  Or, the same folks have to write all the software
Standardization: Internet Engineering Task Force
  Based on working groups that focus on specific issues
  Produces “Request For Comments” (RFCs)
    Promoted to standards via rough consensus and running code
  IETF Web site is http://www.ietf.org
  RFCs archived at http://www.rfc-editor.org
De facto standards: same folks writing the code
  P2P file sharing, Skype, <your protocol here>…

## Slide 12: Layering: The Problem
Many different applications
  email, web, P2P, etc.
Many different network styles and technologies
  Circuit-switched vs packet-switched, etc.
  Wireless vs. wired vs optical, etc.
How do we organize this mess?

## Slide 13: The Problem (cont’d)
Re-implement every application for every technology?
No! But how does the Internet design avoid this?
Skype
SSH
NFS
Radio
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP

## Slide 14: Solution: Intermediate Layers
Introduce intermediate layers that provide set of abstractions for various network functionality & technologies
  A new app/media implemented only once
  Variation on “add another level of indirection”
Skype
SSH
NFS
Packet
radio
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP
Intermediate
layers

## Slide 15: Software System Modularity
Partition system into modules & abstractions:
Well-defined interfaces give flexibility
  Hides implementation - thus, it can be freely changed
  Extend functionality of system by adding new modules
E.g., libraries encapsulating set of functionality
E.g., programming language + compiler abstracts away not only how the particular CPU works …
  … but also the basic computational model
Well-defined interfaces hide information
  Isolate assumptions
  Present high-level abstractions
  But can impair performance

## Slide 16: Network System Modularity
Like software modularity, but:
Implementation distributed across many machines (routers and hosts)
Must decide:
  How to break system into modules
    Layering
  What functionality does each module implement
    End-to-End Principle
  Where state is stored
    Fate-sharing
We will address these choices in turn

## Slide 17: Layering: A Modular Approach
Partition the system
  Each layer solely relies on services from layer below
  Each layer solely exports services to layer above
Interface between layers defines interaction
  Hides implementation details
  Layers can change without disturbing other layers

## Slide 18: Properties of Layers (OSI Model)
Service: what a layer does
Service interface: how to access the service
  Interface for layer above
Protocol (peer interface): how peers communicate to implement the service
  Set of rules and formats that specify the communication between network elements
  Does not specify the implementation on a single machine, but how the layer is implemented between machines

## Slide 19: OSI Layering Model
Open Systems Interconnection (OSI) model
  Developed by International Organization for Standardization (OSI) in 1984
  Seven layers
Internet Protocol (IP)
  Only five layers
  The functionalities of the missing layers (i.e., Presentation and Session) are provided by the Application layer
Transport
Network
Datalink
Session
Presentation
Application
Physical

## Slide 20: Physical Layer (1)
Service: move information between two systems connected by a physical link
Interface: specifies how to send and receive bits
Protocol: coding scheme used to represent a bit, voltage levels, duration of a bit
Examples: coaxial cable, optical fiber links; transmitters, receivers
Transport
Network
Datalink
Physical
Session
Present.
Application
101010100110101110
Physical Layer
Physical Layer
Datalink
layer
Datalink
layer
101010100110101110
Transmission
medium

## Slide 21: Datalink Layer (2)
Service:
  Enable end hosts to exchange frames (atomic messages) on the same physical line or wireless link
  Possible other services:
    Arbitrate access to common physical media
    May provide reliable transmission, flow control
Interface: send frames to other end hosts; receive frames addressed to end host
Protocols: addressing, Media Access Control (MAC) (e.g., CSMA/CD - Carrier Sense Multiple Access / Collision Detection)
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 22: Datalink Layer (2)
Each frame has a header which contains a source and a destination MAC address
MAC (Media Access Control) address
  Uniquely identifies a network interface
  48-bit, assigned by the device manufacturer
101010100110101110
Datalink Layer
Frame
Hdr.
Datalink Layer
Frame
Hdr.
Physical Layer
Physical Layer
101010100110101110
Frame Payload
Frame Payload
Network
Layer
Network
Layer
MAC Dest. Address
MAC Src. Address
…
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 23: MAC Address Examples
Can easily find MAC addr. on your machine/device:
  E.g., ifconfig (Linux, Mac OS X), ipconfig (Windows)
Transport
Network
Session
Present.
Application
Datalink
Physical
Wi-Fi MAC address
Wired/Ethernet MAC address

## Slide 24: Local Area Networks (LANs)
LAN: group of hosts/devices that
  are in the same geographical proximity (e.g., same building, room)
  use same physical communication technology
Examples:
  all laptops connected wirelessly at a Starbucks café
  all devices and computers at home
  all hosts connected to wired Ethernet in an office
Transport
Network
Datalink
Physical
Session
Present.
Application
Ethernet cable and port

## Slide 25: LANs
All hosts in a LAN can share same physical communication media
  Also called, broadcast channel
Each frame is delivered to every host
If a host is not the intended recipient, it drops the frame
Transport
Network
Datalink
Physical
Session
Present.
Application
MAC Addr: A
MAC Addr: B
MAC Addr: C
B
B

## Slide 26: Switches
Hosts in same LAN can be also connected by switches
A switch forwards frames only to intended recipients
  Far more efficient than broadcast channel
Transport
Network
Datalink
Physical
Session
Present.
Application
B
MAC Addr: B
MAC Addr: A
MAC Addr: D
MAC Addr: C
Switch

## Slide 27: Media Access Control (MAC) Protocols
Problem:
  How do hosts access a broadcast media?
  How do they avoid collisions?
Three solutions:
  Channel partition
  “Taking turns”
  Random access
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 28: MAC Protocols
Channel partitioning protocols:
  Allocate 1/N bandwidth to every host
  Share channel efficiently and fairly at high load
  Inefficient at low load (where load = # senders):
    1/N bandwidth allocated even if only 1 active node!
  E.g., Frequency Division Multiple Access (FDMA); optical networks
“Taking turns” protocols:
  Pass a token around active hosts
  A host can only send data if it has the token
  More efficient at low loads: single node can use >> 1/N banwidth
  Overhead in acquiring the token
  Vulnerable to failures (e.g., failed node or lost token)
  E.g., Token ring
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 29: MAC Protocols
Random Access
  Efficient at low load: single node can fully utilize channel
  High load: collision overhead
Key ideas of random access:
  Carrier sense (CS)
    Listen before speaking, and don’t interrupt
    Checking if someone else is already sending data
    … and waiting till the other node is done
  Collision detection (CD)
    If someone else starts talking at the same time, stop
    Realizing when two nodes are transmitting at once
    …by detecting that the data on the wire is garbled
  Randomness
    Don’t start talking again right away
    Waiting for a random time before trying again
  Examples: CSMA/CD, Ethernet, best known implementation
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 30: (Inter) Network Layer (3)
Service:
  Deliver packets to specified network addresses across multiple datalink layer networks
  Possible other services:
    Packet scheduling/priority
    Buffer management
Interface: send packets to specified network address destination; receive packets destined for end host
Protocols: define network addresses (globally unique); construct forwarding tables; packet forwarding
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 31: (Inter) Network Layer (3)
IP address: unique addr. assigned to network device
Assigned by network administrator or dynamically when host connects to network
101010100110101110
Datalink Layer
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Net.
Hdr.
Frame
Hdr.
Physical Layer
Physical Layer
101010100110101110
Net. Payload
Net. Payload
Network Layer
Net.
Hdr.
Network Layer
Net.
Hdr.
Net. Paylaod
Net. Paylaod
Transport
Layer
Transport
Layer
Frame Payload
IP Dest. Address
IP Src. Address
…
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 32: Wide Area Network
Wide Area Network (WAN): network that covers a broad area (e.g., city, state, country, entire world)
  E.g., Internet is a WAN
WAN connects multiple datalink layer networks (LANs)
Datalink layer networks are connected by routers
  Different LANs can use different communication technology (e.g., wireless, cellular, optics, wired)
Transport
Network
Datalink
Physical
Session
Present.
Application
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1

## Slide 33: Routers
Forward each packet received on an incoming link to an outgoing link based on packet’s destination IP address (towards its destination)
Store & forward: packets are buffered before being forwarded
Forwarding table: mapping between IP address and the output link
incoming links
outgoing links
Router
Memory

## Slide 34: Packet Forwarding
Upon receiving a packet, a router
  read the IP destination address of the packet
  consults its forwarding table  output port
  forwards packet to corresponding output port
Transport
Network
Datalink
Physical
Session
Present.
Application
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1
IP B

## Slide 35: IP Addresses vs. MAC Addresses
Why not use MAC addresses for routing?
  Doesn’t scale
Analogy
  MAC address  SSN
  IP address  (unreadable) home address
MAC address: uniquely associated to the device for the entire lifetime of the device
IP address: changes as the device location changes
  Your notebook IP address at school is different from home
Transport
Network
Datalink
Physical
Session
Present.
Application
10 7th Street NW
Washington, DC 21115
1051 Euclid Ave
Berkeley, CA 94722

## Slide 36: IP Addresses vs. MAC Addresses
Transport
Network
Datalink
Physical
Session
Present.
Application
Why does packet forwarding using IP addr. scale?
Because IP addresses can be aggregated
  E.g., all IP addresses at UC Berkeley start with 0xA9E5, i.e., any address of form 0xA9E5**** belongs to Berkeley
  Thus, a router in NY needs to keep a single entry for all hosts at Berkeley
  If we were using MAC addresses the NY router would need to maintain an entry for every Berkeley host!!
Analogy:
  Give this letter to person with SSN: 123-45-6789 vs.
  Give this letter to “John Smith, 123 First Street, LA, US”

## Slide 37: The Internet Protocol (IP)
Internet Protocol: Internet’s network layer
Service it provides: “Best-Effort” Packet Delivery
  Tries it’s “best” to deliver packet to its destination
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
source
destination
IP network
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 38: Transport Layer (4)
Service:
  Provide end-to-end communication between processes
  Demultiplexing of communication between hosts
  Possible other services:
    Reliability in the presence of errors
    Timing properties
    Rate adaptation (flow-control, congestion control)
Interface: send message to specific process at given destination; local process receives messages sent to it
Protocol: port numbers, perhaps implement reliability, flow control, packetization of large messages, framing
Examples: TCP and UDP
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 39: Port Numbers
Port number: 16-bit number identifying the end-point of a transport connection
  E.g., 80 identifies the port on which a processing implementing HTTP server can be connected
Transport
Network
Datalink
Physical
Session
Present.
Application
101010100110101110
Network Layer
Trans.
Hdr.
Net.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Physical Layer
Physical Layer
101010100110101110
Data
Data
Data
Data
Transport Layer
Trans.
Hdr.
Transport Layer
Trans.
Hdr.
Data
Data

## Slide 40: Internet Transport Protocols
Datagram service (UDP)
  No-frills extension of “best-effort” IP
  Multiplexing/Demultiplexing among processes
Reliable, in-order delivery (TCP)
  Connection set-up & tear-down
  Discarding corrupted packets (segments)
  Retransmission of lost packets (segments)
  Flow control
  Congestion control
Services not available
  Delay and/or bandwidth guarantees
  Sessions that survive change-of-IP-address
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 41: Application Layer (7 - not 5!)
Service: any service provided to the end user
Interface: depends on the application
Protocol: depends on the application
Examples: Skype, SMTP (email), HTTP (Web), Halo, BitTorrent …
What happened to layers 5 & 6?
  “Session” and “Presentation” layers
  Part of OSI architecture, but not Internet architecture
  Their functionality is provided by application layer
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 42: Application Layer (5)
101010100110101110
Transport Layer
Trans.
Hdr.
Transport Layer
Trans.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Physical Layer
Physical Layer
101010100110101110
Data
Data
Data
Data
Data
Data
Data
Application Layer
Application Layer
Data

## Slide 43: Five Layers Summary
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Logically, layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 44: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 45: Administrivia
Midterm 3 coming up on Wen 11/28 5:00-6:30PM
  All topics:
    Focus will be on Lectures 18 – 23 and associated readings, and Projects 3
    But expect 20-30% questions from materials from Lectures 1-17
  Closed book
  2 pages hand-written notes both sides

## Slide 46: Break

## Slide 47: The Internet Hourglass
Data Link
Physical
Applications
The Hourglass Model
Waist
There is just one network-layer protocol, IP.
The “narrow waist” facilitates interoperability.
SMTP
HTTP
NTP
DNS
TCP
UDP
IP
Ethernet
SONET
802.11
Transport
Fiber
Copper
Radio

## Slide 48: Implications of Hourglass
Single Internet-layer module (IP):
Allows arbitrary networks to interoperate
  Any network technology that supports IP can exchange packets
Allows applications to function on all networks
  Applications that can run on IP can use any network
Supports simultaneous innovations above and below IP
  But changing IP itself, i.e., IPv6, very involved

## Slide 49: Drawbacks of Layering
Layer N may duplicate layer N-1 functionality
  E.g., error recovery to retransmit lost data
Layers may need same information
  E.g., timestamps, maximum transmission unit size
Layering can hurt performance
  E.g., hiding details about what is really going on
Some layers are not always cleanly separated
  Inter-layer dependencies for performance reasons
  Some dependencies in standards (header checksums)
Headers start to get really big
  Sometimes header bytes >> actual content

## Slide 50: Placing Network Functionality
Hugely influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
“Sacred Text” of the Internet
  Endless disputes about what it means
  Everyone cites it as supporting their position

## Slide 51: Basic Observation
Some types of network functionality can only be correctly implemented end-to-end
  Reliability, security, etc
Because of this, end hosts:
  Can satisfy the requirement without network’s help
  Will/must do so, since can’t rely on network’s help
Therefore don’t go out of your way to implement them in the network

## Slide 52: Example: Reliable File Transfer
Solution 1: make each step reliable, and then concatenate them
Solution 2: end-to-end check and try again if necessary
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 53: Discussion
Solution 1 is incomplete
  What happens if memory is corrupted?
  Receiver has to do the check anyway!
Solution 2 is complete
  Full functionality can be entirely implemented at application layer with no need for reliability from lower layers
Is there any need to implement reliability at lower layers?
  Well, it could be more efficient

## Slide 54: End-to-End Principle
Implementing this functionality in the network:
Doesn’t reduce host implementation complexity
Does increase network complexity
Probably imposes delay and overhead on all applications, even if they don’t need functionality
However, implementing in network can enhance performance in some cases
  E.g., very lossy link

## Slide 55: Conservative Interpretation of E2E
Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level
Unless you can relieve the burden from hosts, don’t bother

## Slide 56: Moderate Interpretation
Think twice before implementing functionality in the network
If hosts can implement functionality correctly, implement it in a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality
This is the interpretation we are using

## Slide 57: Summary (1/2)
Layered architecture powerful abstraction for organizing complex networks
Internet: 5 layers
  Physical: send bits
  Datalink: Connect two hosts on same physical media
  Network: Connect two hosts in a wide area network
  Transport: Connect two processes on (remote) hosts
  Applications: Enable applications running on remote hosts to interact
Unified Internet layering (Application/Transport/ Internetwork/Link/Physical) decouples apps from networking technologies

## Slide 58: Summary (2/2)
E2E argument encourages us to keep IP simple
If higher layer can implement functionality correctly, implement it in a lower layer only if
  it improves the performance significantly for application that need that functionality, and
  it does not impose burden on applications that do not require that functionality