## Slide 1: Network Layer
Computer System Engineering, Fall 2018. (IPADS, SJTU)
All about routing
Yubin Xia

## Slide 2: OSI, TCP/IP & Protocol Stack
7th Application Layer
6th Presentation Layer
4th Transport Layer
3th Network Layer
2nd Link Layer
1st Physical Layer
Application Layer
HTTP
TCP
Ethernet
UDP
IP
PPP
…
SMTP
POP3
FTP
…
ICMP
ARP & RARP
Transport Layer
5th Session Layer
Network Layer
Link Layer
End-to-end Layer
Network Layer
Link Layer
OSI
TCP/IP
CSE
WiFi
Fiber
TD-LTE
FDD
…

## Slide 3: Network Layer

## Slide 4: IP: Best-effort Network
Best-effort network
  If it cannot dispatch, may discard a packet
Guaranteed-delivery network?
  Also called store-and-forward network, no discarding data
  Work with complete messages rather than packets
  Uses disk for buffering to handle peaks
  Tracks individual message to make sure none are lost
In real world
  No absolute guarantee
  Guaranteed-delivery: higher layer; best-effort: lower layer

## Slide 5: Duplicate Packets and Suppression
Discarding packets is common case
  Many network protocol includes timeout and resend mechanism
When a congested forwarder discards a packet
  Client does not receive a response as quickly as originally hoped
  Users may prepared for duplicate requests and responses
  Detecting duplicates may or may not be important

## Slide 6: The Network Layer
Addressing interface
  Network attachment points
  Network address
  Source & destination
NETWORK_SEND (segment_buffer, destnation, network_protocol, end_layer_protocol)
NETWORK_HANDLE (packet, network_protocol)

## Slide 7: Managing the Forwarding Table: Routing
Routing (or path-finding)
  Constructing the tables
Impractical by hand
  Determining the best paths requires calculation
  Recalculating the table when links change
  Recalculating the table when link fails
  Adapt according to traffic congestion
Static routing vs. adaptive routing
  Adaptive routing requires exchange of info
Where are you going?

## Slide 8: IP Route Table
Interface 1 … Interface N

## Slide 9: Control-plane VS. Data-plane
Control-plane
  Control the data flow by defining rules
  E.g., the routing algorithm
Data-plane
  The data-path which copies data according to the rules
  Performance critical
  E.g., the IP forwarding process
The routing table
  Control-plane writes the table, data-plane reads the table

## Slide 10: Routing
How to generate the routing table?

## Slide 11: Goal of A Routing Protocol
Allow each switch to know, for every node dst in the network, a route to dst
Allow each switch to know, for every node dst in the network, a minimum-cost route to dst
Build a routing table at each switch, such that routing_table[dst] contains a minimum-cost route to dst

## Slide 12: Distributed Routing: 3 Steps in General
Nodes learn about their neighbors via the HELLO protocol
Nodes learn about other reachable nodes via advertisements
Nodes determine the minimum-cost routes (of the routes they know about)

## Slide 13: Two Types of Routing Protocol
Protocol 1: Link-state
  Nodes advertise to everyone their costs to their neighbors
    via flooding
  Integrate using Dijkstra's
Protocol 2: Distance-vector
  Nodes advertise to neighbors with their cost to all known nodes
  Update routes via Bellman-Ford integration

## Slide 14: Link-state Routing

## Slide 15: Link-state Routing

## Slide 16: Link-state Routing

## Slide 17: Link-state Routing

## Slide 18: Link-state Routing

## Slide 19: Link-state Routing

## Slide 20: Link-state Routing

## Slide 21: Link-state Routing

## Slide 22: Link-state Routing

## Slide 23: Link-state Routing

## Slide 24: Link-state Routing

## Slide 25: Link-state Routing

## Slide 26: Link-state Routing

## Slide 27: Link-state Routing

## Slide 28: Distance-vector Routing

## Slide 29: Distance-vector Routing

## Slide 30: Distance-vector Routing

## Slide 31: Distance-vector Routing

## Slide 32: Problem: Do not Scale to the Internet
Link-State
  Pro: Fast convergence
  Cons: high overhead because of flooding
  Good for SJTU-sized networks, but not the Internet
Distance Vector
  Pro: Low overhead
  Cons: Convergence time is proportional to longest path
  Good for small networks

## Slide 33: 3 Ways to Scale
Path-vector Routing
  Advertisements include the path, to better detect routing loops
Hierarchy of Routing
  Route between regions, and then within a region
Topological Addressing
  Assign addresses in contiguous blocks to make advertisements smaller

## Slide 34: Path Vector Exchange
Each participant maintains a path vector
  A complete path to some destination
  E.g., zero-length path to itself
  Gradually learns about other paths
  Construct a new forwarding table from its new path vector
Algorithm
  Advertising
  Path selection

## Slide 35: Path Vector Exchange
Need coordination to ensure no loop
A
G

## Slide 37: Path Vector Exchange
Better for scaling
  Like Distance-Vector, but include the full path in the routing advertisements
  Overhead increases (advertises are larger), but convergence time decreases (avoid counting to infinity)
  Overhead is still lower than Link-State

## Slide 38: Question on Path Vector
How do we avoid permanent loops?
  When a node updates its paths, it never accepts a path that has itself
What happens when a node hears multiple paths to the same destination?
  It picks the better path
What happens if the graph changes?
  Algorithm deals well with new links
  To deal with links that go down, each router should discard any path that a neighbor stops advertising

## Slide 39: Hierarchical Address Assignment & Routing
Two problems of the path vector implementation
  Every attachment point must have a unique address
  The path vector grows in size with the number of attachment points
Hierarchy for better scalability
  Two parts of network address: region & station, e.g., "11,75"
  Regions correspond to the set of closely-connected entities
  E.g., region-11 has only 1 entry in other region routers' table

## Slide 40: Hierarchical Address Assignment & Routing
Region is also as known as AS: Autonomous System

## Slide 41: Hierarchical Address Assignment & Routing
Problems introduced by hierarchy: more complex
  Binding address with location
    Has to change address after changing location
  Paths may no longer be the shortest possible
    Algorithm has less detailed information
More about hierarchy
  Can extend to more levels
  Different places can have different levels

## Slide 42: Routing Hierarchy
Across Region
  Use one routing protocol to route across regions, and a different protocol to route within regions
  Implies that there are devices on the edge of each region that can "translate" between or "speak" both protocols
BGP is the path-vector protocol used across regions
  Border Gateway Protocol

## Slide 43: Topological Addressing
Further reduce the routing table
  Despite being between regions, BGP still routes to IP addresses (e.g., to 18.0.0.1, not to region-3 )
  Addresses are given to regions in contiguous blocks, so that they can be specified succinctly via a particular notation ("CIDR" notation)
    CIDR: Classless Inter Domain Routing
  Keeps advertisements small
CIDR Notation

## Slide 44: Data Plane: Packet Forwarding

## Slide 45: Network Layer Interface
structure packet
bit_string source
bit_string destination
bit_string end_protocol
bit_string payload

## Slide 46
1 procedure NETWORK_SEND (segment_buffer, destination,
2 net_protocol, end_protocol)
3 packet instance outgoing_packet
4 outgoing_packet.payload ← segment_buffer
5 outgoing_packet.end_protocol ← end_protocol
6 outgoing_packet.source ← MY_NETWORK_ADDRESS
7 outgoing_packet.destination ← destination
8 NETWORK_HANDLE (outgoing_packet, net_protocol)
9 procedure NETWORK_HANDLE (net_packet, net_protocol)
10 packet instance net_packet
11 if net_packet.destination != MY_NETWORK_ADDRESS then
12 next_hop ← LOOKUP (net_packet.destination, forwarding_table)
13 LINK_SEND (net_packet, next_hop, link_protocol, net_protocol)
14 else
15 GIVE_TO_END_LAYER (net_packet.payload,
16 net_packet.end_protocol, net_packet.source)

## Slide 47
sendproc
NETWORK_SEND
NETWORK_HANDLE
GIVE_TO_END_LAYER
LINK_SEND
GIVE_TO_NETWORK
_HANDLER
LINK_RECEIVE
sendproc
net_handler[]
link_protocol[]
LOOKUP
struct packet
source
destination
end_protocol
payload
struct frame
struct checked_cnt
net_protocol
payload
checksum

## Slide 48: Forwarding an IP Packet
Lookup packet's DST in forwarding table
  If known, find the corresponding outgoing link
  If unknown, drop packet
Decrement TTL (Time To Live)
  Drop packet if TTL is zero
Update header checksum
Forward packet to outgoing port
Transmit packet onto link

## Slide 49: Data-plane Case Study: Intel's DPDK
DPDK: Data Plane Development Kit
Network card
  Has several ports
  A port has RX/TX
Processor
  Read packets from RX
    Polling
  Find output port
  Write packets to TX
RX for receiving
TX for sending

## Slide 50: NAT

## Slide 51: NAT (Network Address Translation)
Private network
  Public routers don't accept routes to network 10
NAT router: bridge the private networks
  Router between private & public network
  Send: modify source address to temp public address
  Receive: modify back by looking mapping table
Limitations
  Some end-to-end protocols place address in payloads
  The translator may become the bottleneck
  What if two private network merge?

## Slide 52: NAT

## Slide 53: NAT (Network Address Translation)
Private network
  Public routers don't accept routes to network 10
NAT router: bridge the private networks
  Router between private & public network
  Send: modify source address to temp public address
  Receive: modify back by looking mapping table
Limitations
  Some end-to-end protocols place address in payloads
  The translator may become the bottleneck
  What if two private network merge?

## Slide 54
Src IP: 192.168.1.2
Dst IP: 173.194.72.104
Src Port: 54321
Dst Port: 80
Data
Src IP: 202.120.40.85
Dst IP: 173.194.72.104
Src Port: 60001
Dst Port: 80
Data
Netgate
192.168.1.1
202.120.40.85
173.194.72.104
Src IP: 173.194.72.104
Dst IP: 192.168.1.2
Src Port: 80
Dst Port: 54321
Data
Dst IP: 202.120.40.85
Src IP: 173.194.72.104
Src Port: 80
Dst Port: 60001
Data
Src IP | Src Port | NAT Port
192.168.1.2 | 54321 | 60001
192.168.1.2 | 12345 | 60002
... |  | 
192.168.1.2

## Slide 55: CASE: Ethernet Mapping
Mapping Internet to Ethernet

## Slide 56: Case Study: Mapping Internet to Ethernet
Listen-before-sending rule, collision
Ethernet: CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
Ethernet type
  Experimental Ethernet, 3 mpbs
  Standard Ethernet, 10 mbps
  Fast Ethernet, 100 mbps
  Gigabit Ethernet, 1000 mbps
Notes: 基带冲突检测的载波监听多路访问技术(载波监听多点接入/碰撞检测)

## Slide 57: Overview of Ethernet
A half duplex Ethernet
  The max propagation time is less than the 576 bit times, the shortest allowable packet
  So that two parties can detect a collision together
  If collision: wait random first time, exponential backoff if repeat
A full duplex & point-to-point Ethernet
  No collisions & the max length of the link is determined by the physical medium

## Slide 58: Difference between Hub and Switch
Hub
  A frame is "broadcast" to every one of its ports
  A 10/100Mbps hub must share its bandwidth with each port
Switch
  Keeps a record of the MAC addresses of all the devices
  A 10/100Mbps switch will allocate a full 10/100Mbps to each of its ports

## Slide 59: Broadcast Aspects of Ethernet
Broadcast network
  Every frame is delivered to every station
  (Compare with forwarding network)
ETHERNET_SEND
  Pass the call along to the link layer
ETHERNET_HANDLE
  Simple, can even be implemented in hardware

## Slide 60: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet
no need to do any forwarding

## Slide 61: Broadcast Aspects of Ethernet
procedure ETHERNET_HANDLE (net_packet, length)
destination ← net_packet.target_id
if destination = my_station_id
or destination = BROADCAST_ID
then
GIVE_TO_END_LAYER (net_packet.data,
net_packet.end_protocol,
net_packet.source_id)
else
ignore packet

## Slide 62: Layer Mapping: Attach Ethernet to Forwarding Network
L sends a RPC to N by sending to station 18 of link 1
L sends a RPC to E by sending to K, E may have 15 as address, as well as M
15

## Slide 63: Layer Mapping
The Internet network layer
  NETWORK_SEND (data, length, RPC, INTERNET, N)
  NETWORK_SEND (data, length, RPC, ENET, 18)
L must maintain a table

## Slide 64: ARP (Address Resolution Protocol)
NETWORK_SEND ("where is M?", 11, ARP, ENET, BROADCAST)
NETWORK_SEND ("M is at station 15", 18, ARP, ENET, BROADCAST)
L asks E's Ethernet address, E does not hear the Ethernet broadcast, but the router at station 19 does, and it sends a suitable ARP response instead
Manage forwarding table as a cache

## Slide 65: ARP & RARP Protocol
Name mapping: IP address <-> MAC address

## Slide 66: ARP & RARP

## Slide 67: Network Topology
Take SJTU network for example
  Subnet: usually like 192.168.0.2 or 10.0.0.2
  Gateway: usually like 192.168.0.1
    Get the global IP address: 202.120.40.82
    A gateway usually has two (or more) IP address
  Proxy: get proxy's address
    E.g., 106.185.46.164 (Japan)

## Slide 68: Network Topology
A
B
C
G
Proxy
Google
Gateway
Baidu
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.1
    202.120.40.82
106.185.46.164
220.181.57.217
173.194.38.198

## Slide 69: How to Use socket to Access www.baidu.com ?
C
Baidu
192.168.0.4
220.181.57.217
You code as if your PC connect directly with Baidu
  Call connect() with Baidu's IP address
But how does the system find next hop?

## Slide 70: Putting All Together
App: I want to send a packet to Baidu, here is the packet with Baidu's IP in its header as target IP, and client's IP as source IP (Node-C)
OS: I don't know how to get to Baidu, I'll just send it to the router (gateway). But I cannot change the source IP of the packet, so I'll just change the MAC target address of the packet to the router's MAC address
Data
Target IP: Baidu's IP
Source IP: Node-C
Target MAC:
Source MAC:
Data
Target IP: Baidu's IP
Source IP: Node-C
Target MAC: Gateway
Source MAC: Node-C

## Slide 71: Putting All Together
The router-1 (gateway): I get a packet with my MAC as target address. Is it my IP? No… So I'll just forward it to next hop, by changing the target MAC address to next hop's MAC address (NAT: change source IP and source port as well)
Router-2: I connect directly to Baidu, I'll just change the target MAC address to Baidu
Data
Target IP: Baidu's IP
Source IP: Node-C
Target MAC: Gateway
Source MAC: Node-C
Data
Target IP: Baidu's IP
Source IP: Router-1
Target MAC: Router-2
Source MAC: Router-1
Data
Target IP: Baidu's IP
Source IP: Router
Target MAC: Baidu
Source MAC: Router-2

## Slide 72: ARP Spoofing
Construct spoofed ARP replies
A target computer could be convinced to send frames destined for computer A to instead go to computer B
Computer A will have no idea that this redirection took place
This process of updating a target computer's ARP cache is referred to as "ARP poisoning"

## Slide 73
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 74
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
A's cache is poisoned

## Slide 75: ARP Spoofing
Now all the packets that A intends to send to B will go to the hacker's machine
Cache entry would expire, so it needs to be updated by sending the ARP reply again
  How often?
  depends on the particular system
  Usually every 40s should be sufficient
In addition the hacker may not want his Ethernet driver talk too much
  Accomplish with ifconfig -arp

## Slide 76: Man-in-the-Middle Attack
A hacker inserts his computer between the communications path of two target computers
The hacker will forward frames between the two target computers so communications are not interrupted
E.g., Hunt, Ettercap, etc.
  Can be obtained easily in many web archives

## Slide 77: Man-in-the-Middle Attack
The attack is performed as follows:
  Suppose X is the hacker's computer
  T1 and T2 are the targets
  X poisons the ARP cache of T1 and T2
  T1 associates T2's IP with X's MAC
  T2 associates T1's IP with X's MAC
  All of T1 and T2's traffic will then go to X first, instead of directly to each other

## Slide 78
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 79
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
T1's cache is poisoned

## Slide 80
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc

## Slide 81
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
T2's cache is poisoned

## Slide 82
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Message intended to send to T2
Hacker will
relay the
message

## Slide 83
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Hacker will relay the message
Message
intended to
send to T1

## Slide 84: Defenses against ARP Spoofing
No Universal defense (!)
Use static ARP entries
  Cannot be updated
  Spoofed ARP replies are ignored
  ARP table needs a static entry for each machine on the network
  Large overhead
    Deploying these tables
    Keep the table up-to-date

## Slide 85: Arpwatch
A free UNIX program which listens for ARP replies on a network
Build a table of IP/MAC associations and store it in a file
When a MAC/IP pair changes (flip-flop), an email is sent to an administrator
Some programs, such as Ettercap, cause only a few flip flops is difficult to be detected on a DHCP-enabled network, where flip flops occur at regular intervals