## Slide 1: I/O
Yubin Xia
IPADS, SJTU
ACKs: Some slides are adapted from the textbook’s original slides and frans’s os course notes

## Slide 2: Review: What Can’t You Do in an Interrupt Handler?
You cannot sleep
  or call something that might sleep
You cannot refer to current
You cannot allocate memory with GPF_KERNEL (which can sleep), you must use GPF_ATOMIC (which can fail)
You cannot call schedule()
You cannot do a down() semaphore call
  However, you can do an up()
You cannot transfer data to/from user space
  E.g., copy_to_user(), copy_from_user()

## Slide 3: Review
  FlexSC: Exception-less syscall: remove synchronicity by decoupling invocation from execution
  Why I/O sub-system: Thousands of devices, each slightly different
  Unified interface: file
    Open, read, write, seek, close, …
    Avoid too generalization
  Top-half & bottom-half

## Slide 4
The two main jobs of a computer are I/O and processing. In many cases, the main job is I/O, and the processing is merely incidental.
—— Operating System Concepts, 8th edition

## Slide 5: I/O

## Slide 6: Why do we Need an I/O Subsystem
Thousands of devices, each slightly different
  How can we standardize the interfaces to these devices?
Devices are unreliable
  Media failures and transmission errors
  How can we make them reliable?
Devices are unpredictable and/or slow
  How can we manage them if we don’t know what they will do or how they will perform?

## Slide 7: Device Rates Vary Many Orders of Magnitude
I/O subsystem better handle this wide range
  Better not have high overhead/byte for fast devices!
  Better not waste time waiting for slow devices

## Slide 8: Goal of I/O Subsystem
Provides uniform interfaces, despite wide range of different devices
  This code works on many different devices:
  FILE fd = fopen(“/dev/something”,”rw”); for (int i = 0; i < 10; i++) { fprintf(fd,”Count %d\n”,i); } close(fd);
  Why?
  Because code that controls devices (“device driver”) implements standard interface.
Provides a layer of abstraction of I/O hardware
  Manages and interacts with hardware
  Hides hardware and operation details
Notes: 键盘、显示器、U盘为什么是文件？
游戏手柄？
Lidar？
Socket反例：send/recv
I/O device has its own CPU?

## Slide 9: Three Types of Device Interfaces
Three common types of device interfaces
  Character devices
  Block devices
  Network devices

## Slide 10: Character Devices
Character Devices
  Example: keyboard/mouse, serial port, some USB devices
  Sequential access, single characters at a time
  I/O commands: get(), put(), etc.
  Often use open file interface and semantics

## Slide 11: Press ‘a’ to display ‘a’

## Slide 12
Function pointer

## Slide 13
#define C(x) ((x)-’@’) // Control-x
kbdgetc()

## Slide 16: I/O instruction in xv6

## Slide 17
Notes: UART: Universal Asynchronous Receiver/Transmitter (即串口)

## Slide 19: Block Devices
Block Devices
  Example: disk drive, tape drive, DVD-ROM
  Uniform block I/O interface to access blocks of data
  Raw I/O or file-system access
  Memory-mapped file access possible

## Slide 20: Network Devices
Network Devices
  Examples: Ethernet, wireless, bluetooth
  Different enough from block/character to have own interface
  Provide special networking interface for supporting various network protocols
  For example, send/receive network packets

## Slide 21: How Does User Deal with Timing?
Blocking I/O: “Wait”
  When request data (e.g. read() system call), put process in waiting state until data is ready
  When write data (e.g. write() system call), put process in waiting state until device is ready for data
Non-blocking I/O: “Don’t Wait”
  Returns immediately from read or write request with count of bytes successfully transferred
  Read may return nothing, write may write nothing
Asynchronous I/O: “Tell Me Later”
  When request data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When send data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 22: Synchronous and Asynchronous I/O

## Slide 23: Steps in a DMA Transfer

## Slide 24: I/O Device Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O operation has encountered an error
Two methods
  Polling
  Interrupt-driven
Polling:
  I/O device puts completion/error information in device-specific status register
  OS periodically checks the status register
  Pro: low overhead
  Con: may waste many cycles on polling if infrequent or unpredictable I/O operations
Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when:
(a) The I/O device has completed the operation.
(b) Or when the I/O device has encountered an error.
This can be accomplished in two different ways: Polling and I/O interrupt.
+1 = 58 min. (Y:38)

## Slide 25: Interrupt Driven
Pro: handles unpredictable events well
Con: interrupts relatively high overhead
Some devices may combine both polling and interrupt-driven
  High-bandwidth network device example:
    interrupt for first incoming packet
    polling for following packets until hardware empty

## Slide 26: Interrupt-Driven I/O Cycle

## Slide 27: A Kernel I/O Structure

## Slide 28: Device Drivers
Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device drivers typically divided into two pieces:
  Top half
  Bottom half

## Slide 29: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 30: Recall : Read Disk
readi()->bread()
  Call bget() to read from buffer cache first
  If not found, call iderw() to read from disk, and mark as valid.

## Slide 31: Xv6 disk driver design & Implementation
Design Overview
  Support an IDE driver
  Use I/O Instructions instead of Memory Mapped I/O
    in, out
  Asynchronous I/O model
    Use a simple queue of I/O request
    Use interrupt to notify the available of data

## Slide 32: IDE Specification
Xv6 uses a relative old IDE specification
  Not PCI negotiation
IDE Ports
  0x1F0-0x1F7
    0x1f0: write/read port
    0x1f2: number of sectors
    0x1f3-0x1f5: sector number
    0x1f6: diskno and sector number
    0x1f7: command registers, status bit
  0x3F6 interrupt control line

## Slide 33: Polling Mechanism

## Slide 34: IDE Initialization

## Slide 35: Synchronous I/O (iderw)

## Slide 39: Sleep and Wakeup Mechanism in xv6

## Slide 40: IDE.c
The driver can only handle 1 operation at a time
  Only send the buffer at the front of the queue
  Others are simply waiting their turn
iderw() maintains a queue of requests
  Adds the buffer b to the end of the queue
  If b is the first, then call idestart(), if not, just wait
  Then just sleep, instead of polling
ideintr() will handle the first request
  Then start other request if any

## Slide 41: Homework
Please read xv6 code and describe the process of helloworld (from “./hello” to the exit)